## Slide 1: Vertical Take-off Landing (VTOL) Aircraft
Metin Öz Harun Üner Ömer Karataş
2019405000 2019405207 2019405033

## Slide 2: Problem Definition and Functional Requirements :
The aim of the project is to design a fixed wing vtol which can perform transition from hover flight to forward flight by using tilt-rotor mechanism. The aircraft should also follow the functional requirements given below.
Semi-Autonomous Flight
Tilt Rotor mechanism
Wing-Span: 1000-1500mm []
Stall Speed: 8-10m/s []
Cruise Speed: 10-13m/s []
Take-off Weight: 1000-2000gr []
Mostly 3D Printed Manufacturing

## Slide 3: Product Design Specifications
Control Stability
Unusable Rotors
Transition Capabilities
Hover Efficiency

## Slide 4: Tilting Mechanism:
Brushless Servo Motor
Motor
Mostly 3D Printed Manufacturing:
Fuselage
Wing
V-Tail

## Slide 5: XFLR 5 Analysis of the Produced Prototype
Longitudinal Modes
Short Period Longitudinal
Phugoid

## Slide 6: XFLR 5 Analysis of the Produced Prototype
Lateral Modes
Roll Damping
Dutch Roll
Spiral

## Slide 7: Parts of the Wing Section
There are 7 sections to be 3D Printed for each wing
They were cutted from the final design
Necessary updates have been made at the merge zones

## Slide 9
Snap-Joint connection tabs are indicated as yellow.
-Creates larger surface areas for adhesives
-Prevents collapse of walls at connectios
Pin holes are indicated as red.
-They are designed to fit 1.75mm filament pins
-Simplifies alignment and creates strong attachment points
Aileron Connection Lugs

## Slide 10: Printing Times of the parts
Wing_L_P1 | 12h 50min
Wing_L_P2 | 12h 12min
Wing_L_P3 | 9h 26min
Wing_L_P4 | 7h 47min
Winglet_L | 2h 15min
Aileron_L_P1 | 3h 16min
Aileron_L_P2 | 3h 20min
Total (x2) | 102h 12min
It takes 7 days to print all wing parts. Ailerons and part 4 is printed several times due to printing problems.

## Slide 11
Not glued only snap joint holds them together
One side of the printed wing weighs only 347g

## Slide 12: Manufacturing of Fuselage
Fuselage_P1 | 16h 5min
Fuselage_P2 | 15h 40min
Fuselage_P3 | 6h 10min
Front_Cap | 4h 20min
Rear_Cap | 3h 8min
Total (x2) | 45h 23min
It takes 3 days to print all Fuselage parts. There was no problem encountered.

## Slide 13: Assembly of Wing
Gluing wing parts
Gluing wing arm
Parts are aligned using pins.
Attached together using glue.

## Slide 14: Assembly of Wing
Two part glue activator
Assembled wing
Two part glue is used for attaching parts.
Glass fiber pipe is added.

## Slide 15: Changes in the design of V-Tail
Better adhesion
Better durability
Ease of printing

## Slide 16: Assembly of V-Tail

## Slide 17: Assembly of Fuselage

## Slide 18: Assembly of VTOL

## Slide 19: Furthermore:
Aircraft assembly
Electronics wiring and connections
Software configuration
Test flights

## Slide 20: Gannt Chart

## Slide 21: Cost analysis
The cost was calculated ~22000₺ at the first Semester.
It is managed to reduce cost by 30% after detailed market research.