## Slide 1: Vertical Take-off Landing (VTOL) Aircraft
Metin Öz Harun Üner
2019405000 2019405207

## Slide 2: What is VTOL?
-VTOL is a type of aircraft that can take off and land vertically and also perform forward flight like a fixed wing.
-The Types of fixed-wing VTOLs :
Quad-in-Plane VTOL drones
Tail-sitter VTOL drones
Tiltrotor VTOL drones

## Slide 3: Problem Definition and Functional Requirements :
The aim of the project is design a fixed wing vtol which can perform transition from hover flight to forward flight by using tilt-rotor mechanism. The aircraft should also follow the functional requirements given below.
Semi-Autonomous Flight
Tilt Rotor mechanism
Wing-Span: 1000-1500mm []
Stall Speed: 8-10m/s []
Cruise Speed: 10-13m/s []
Take-off Weight: 1000-2000gr []
Mostly 3D Printed Manufacturing

## Slide 5: Concepts of Fixed Wing VTOLs
Concept 1
3 rotors
2 front rotors are able to tilt in y-axes
Only 1 (Rear) passive rotor causes extra drag during horizontal flight
Quite Stable for vertical flight (3-point stability triangle)
Less bending moment on wings

## Slide 6
Concept 3
Concept 2
4 rotors, 2 of them (Front) are able to tilt
2 passive rotor causes extra drag during horizontal flight
Extra weight for rotor arm tubes
Most stable concept for vertical flight
2 rotors, both are able to tilt
No passive rotor, no extra drag
Highest bending moment on wing
Least stable concept for vertical flight

## Slide 7: Product Design Specification
Maintenance
Size Restriction
Weight Control Stability
Aesthetic
Manufacturability
Reliability
Unusable Rotors
Transition Capabilities
Hover Efficiency
Material Cost

## Slide 8: Binary Dominance Matrix

## Slide 9: Concept Evaluation

## Slide 10: Airfoil Selection
NACA 4412
NACA 2412
NACA 6412
Low Drag Coefficient
High Ratio
Low Chamber-Ease of Manufacturing
airfoiltools.com web tool is used to select airfoil, compare and understand their strengths for our design.

## Slide 11: XFLR-5 Wing Design and Analysis
Wing Area: 19.1
M.A.Chord: 191
Airfoil: NACA 4412
Wing Area: 25.0
M.A.Chord: 191
Airfoil: NACA 4412
Wing Area: 25.2
M.A.Chord: 195
Airfoil: NACA 6412
Wing Area: 21.0
M.A.Chord: 191
Airfoil: NACA 4412
Wing Area: 25.0
M.A.Chord: 191
Airfoil: NACA 6412
Wing Area: 262
M.A.Chord: 186
Airfoil: NACA 6412
Increase of wing area
Increase of wing area
Change to higher
Increase of Root Chord
Addition of winglets

## Slide 12: Final Design and Results
XFLR-5
6 Iteration is performed for
different geometries
Final Iteration:
-Wing Span: 1640mm
-M.A.C: 186mm
-Stall Speed: 8.9m/s @ α=9˚
-Cruse Speed: 13m/s @ α=0˚
(for 1500 g take-off weight)

## Slide 13: Furthermore